## Slide 1: Ocean circulation
With Satellite Altimetry and GOCE
Shivam Pandey 17807671
Sarvesh Chaudhary 170637

## Slide 2: Satellite Altimetry
Sea Surface Height [h]

## Slide 3
Herceg et.al

## Slide 4: Gravity Field and Steady-State Ocean Circulation Explorer

## Slide 5: Geoid from GOCE [N]
Provides the Gravity measurement with higher spatial resolution.
Previously used GRACE was meant to provide higher temporal resolution but due to use of larger wavelength was unable to provide much better precision on higher spatial resolution.

## Slide 6: Mean Dynamic Topography
IDT = SSH – Geoid
SSH is disturbed by local factors like moving objects etc.
MDT = mean SSH – Geoid
Repeated Track Method is applied to the Satellite Altimetry.
Proceed with the stationary geoid assumption
Christian, Carl

## Slide 7: Data Filtering
Due to several remaining error sources, geodetic MDTs are usually filtered before ocean currents are calculated.
Gaussian (Binghum 2014)
Other Spatial Averaging (Binghum 2014)
Non-Liner diffusion [Used for steep gradients](Binghum 2010)

## Slide 8
MDT

## Slide 9: Expected Results

## Slide 10: Steps to Follow
Geoid
Get the Geoid (stationary assumption) N
SSH
Compute the time average for the Sea surface height n
MDT
Get the Mean Dynamic Topography (MDT) n-N
Filter
Filter the MDT to remove the noise and residual errors
Current
Get the current components for each of the grid u, v
PCA
Try to track the trends in the currents either by Principal Component Analysis or some other model.

## Slide 11: Dataset

## Slide 13: SSH Data for JASON2 and SARAL

## Slide 16: Say Hi to GOCEAN
A Library to Probe-inside Ocean Currents

## Slide 18: Modules in GOCEAN
I/O
geoid
SSHIO
Preprocessing
Noise Filtering
Smoothing
Currents
MDT
Components
Analysis
K-means clustering
PCA dimension change
GeoidIO
Altimetry

## Slide 19: SSH Data Acquisition with OpenADB

## Slide 20: GeoidIO

## Slide 21: SSHIO
Create a grid like Geoid-grid 1x1.
For each readings of SSH get the closest location in the grid.
Apply average for each point.

## Slide 22: Added Data for SARAL

## Slide 23: SSH Temporal Mean and Geoid

## Slide 24: MDT calculated with JASON2 Data

## Slide 25: MDT after outlier removal

## Slide 26: MDT filtered 2D Gaussian
Notes: Gaussian filtering
Mean dynamic topography

## Slide 27
Latitude
MDT
Longitude

## Slide 28: OCEAN Currents

## Slide 29: Ocean Currents
Notes: Differentiating MDT wrt longitude and lattitude

## Slide 30: Visualize it Closer

## Slide 32: Clustering for Excess Interpretation [Experimental]

## Slide 33: Reasons of k-means not working
The chaotic data at the boundaries.
Time lapse of the data is too small for any pattern.
The extent of data needs to be more.

## Slide 34: References

## Slide 35: Thank You